## Slide 1: Road Network Improvement Using Universal Resilience Patterns
Roman Nett

## Slide 2: Overview
Previous Work
Motivations
Dataset
Metrics
Methods
Results
Conclusions
Future Work

## Slide 3: Previous Work
Universal resilience patterns in complex networks
Jianxi Gao, Baruch Barzel & Albert Barabási
Resilience describes the stability of a network to perturbations

## Slide 4: Previous Work
Different networks have different
points of failure
Rarely predictable

## Slide 5: Previous Work
Bridged the theoretical gap by deriving a universal resilience function of this form
Obtained by combining multiple 1D single component approximation equations that were used in the past
F(xi) and G(xi, xj) describe the laws that govern the components themselves
Aij represents the interactions (adjacency matrix)

## Slide 6: Previous Work
Found the point of bifurcation based solely on the network’s features
Resilience could now be predicted!
Notes: Red is node loss, green is link loss, blue is weight loss

## Slide 7: Previous Work
Topological effects cause by this term
Density + Symmetry*Heterogeneity

## Slide 8: Previous Work
Most resilient with high density, high symmetry, high heterogeneity
Least resilient with low density low symmetry (-1), high heterogeneity
Critical points are not altered

## Slide 9: Motivations
Network resilience is nice and all but can improving the resilience improve the general performance of a network?
I have put this to the test by experimenting on a road network

## Slide 10: Dataset
Minnesota Road Network
2,642 Nodes
3,303 Edges
Largest Component: 2,640 Nodes

## Slide 11: Dataset
Average Degree: 2.500
Min Degree: 1
Max Degree: 5

## Slide 12: Metrics
Resilience
  Size of the Largest Component
Classic
  Network Diameter
  Average Path Length
New Metrics
  Average Congestion
  Car Flow
Previous Work
  Density
  Heterogeneity
  Symmetry

## Slide 13: Metrics - Resilience

## Slide 14: Metrics - Classic
BFS to determine the shortest path between each pair of nodes

## Slide 15: Metrics - Average Congestion
Again using BFS to find the shortest path between each pair of nodes

## Slide 16: Metrics - Car Flow
Maximum Flow:
The maximum amount of “stuff” that can travel from a source node to a sink node through
edge capacities
Home Nodes and Destination Nodes
Home Nodes have smaller degree
Destination Nodes have larger degree
~75% Home Nodes and ~25% Destination Nodes

## Slide 17: Metrics - Car Flow
75.02% Home Nodes
Edge capacities are inversely proportional to edge costs
scipy.sparse.csgraph.maximum_flow

## Slide 18: Metrics - Previous Work
Density grows proportionally with average degree
Heterogeneity
Symmetry is always 1 for undirected graphs

## Slide 19: Methods - Procedure
Measure all metrics for original network
Perturb network to observe phase shift
  Repeat for 10 trials
Partially increase density and perturb
Fully increase density and perturb
Partially increase heterogeneity and perturb
Fully increase heterogeneity and perturb
Fully increase both and perturb
Measure all metrics for fully increased density, heterogeneity, both

## Slide 20: Methods - Perturbing
Node removal
Choose a random node
Remove it and all its links from the network
Link removal
Choose a random link
Remove it from the network

## Slide 21: Methods - Increasing Density
Add more triangles to the network
Choose a random node
Add a link to one of its neighbor’s neighbors
A
B
C

## Slide 22: Methods - Increasing Heterogeneity
Goal is to have large hubs with lots of small degree nodes
Choose random node
If it has degree above three: create a triangle with a neighbor’s neighbor
If it has degree three or below:
Remove an edge
Connect to the closest hub
B
A

## Slide 23: Results - Initial Metrics
Average Congestion | 112,576 ~3.23%
Max Congestion | 948,438 ~27.23%
Car Flow | 51,626
Diameter | 902
Average Distance | 253
Density | 2.500
Heterogeneity | 0.299

## Slide 24: Results - Node Removal
Initial Network
Average of 512.6 nodes

## Slide 25: Results - Link Removal
Initial Network
Average of 698.5 links

## Slide 26: Results - Density Increase

## Slide 27: Results - Partial Density Increase
New Density of ~4.866
Average of 705.5 nodes

## Slide 28: Results - Full Density Increase
New Density of ~7.232
Average of 860.8 nodes

## Slide 29: Results - Combined

## Slide 30: Results - Heterogeneity Increase

## Slide 31: Results - Heterogeneity Increase

## Slide 32: Results - Partial Heterogeneity Increase
New H of ~1.022
Average of 705.0 nodes

## Slide 33: Results - Full Heterogeneity Increase
New H of ~1.324
Average of 708.0 nodes

## Slide 34: Results - Combined

## Slide 35: Results - Both Increase

## Slide 36: Results - Both Increase

## Slide 37: Results - Both Increase

## Slide 38: Results - Both Increase
Final H of ~ 0.794
Final density of ~8.240
Average of 1258.0 nodes

## Slide 39: Results - Metrics for Density Increase
 |  | Old
Average Congestion | 17,286 ~0.50% | 112,576 ~3.23%
Max Congestion | 627,554 ~18.02% | 948,438 ~27.23%
Car Flow | 74,555 | 51,626
Diameter | 862 | 902
Average Distance | 240 | 253

## Slide 40: Results - Metrics for Heterogeneity Increase
 |  | Old
Average Congestion | 15,430 ~0.44% | 112,576 ~3.23%
Max Congestion | 802,194 ~23.03% | 948,438 ~27.23%
Car Flow | 94,451 | 51,626
Diameter | 893 | 902
Average Distance | 253 | 253

## Slide 41: Results - Metrics for Both Increase
 |  | Best
Average Congestion | 9,708 ~0.28% | 15,430 ~0.44% (H)
Max Congestion | 583,177 ~16.74% | 627,554 ~18.02% (D)
Car Flow | 101,334 | 94,451 (H)
Diameter | 866 | 862 (D)
Average Distance | 240 | 240 (D)

## Slide 42: Conclusions - Reproduction
Successfully reproduced the results of the paper
Resilience increased as density and heterogeneity increased
Maximum resilience was reached with high density and high heterogeneity

## Slide 43: Conclusions
Improving the resilience of the road network has improved the performance!
Average Congestion lowered by over 10x
Car flow almost doubled
At the same time, diameter and average path length reduced

## Slide 44: Future Work - Limitations
Small sample size
Undirected
Road performance measures

## Slide 45: Future Work - Extensions
Limitation addressing
Optimization
Opposite Direction

## Slide 46: Thank you for your attention
Questions?

## Slide 47: Citations
Gao, Jianxi & Barzel, Baruch & Barabasi, Albert-Laszlo. (2016). Universal resilience patterns in complex networks. Nature. 530. 307-312. 10.1038/nature16948.
Gleich, David. (2014). Minnesota road network. Stanford. https://www.cise.ufl.edu/research/sparse/matrices/Gleich/minnesota