## Slide 1: From data to complex network control of airline flight delays
Long guo

## Slide 2: setup
The complex network that generated by massive data sets is hard to control. It needs a formal definition for its network dynamics to control such network.
To show how to use a new framework to delineate network dynamics via implementing a new framework to a complex and practical example, which is the passenger airline networks of the United States, and try to control its flight delays, which are the most common failures in these networks.

## Slide 3: Previous works
Agent-based model
Predictive models
  Statistical analysis
  Probabilistic model
  Operational research
  Machine learning

## Slide 4: Methods—Overview
Two main component:
  Model of the dynamic of flight delays
  Method for defining an optimal control strategy for dynamic of flight delays

## Slide 5: Method—flight delay networks
Figure 1A: Flowchart of the framework for flight delay mitigation.
Figure 1B: Sample graph of a circular route and the pie shows the fixed cost of renting a sample aircraft.
Figure 1C: shows the scheduled time of flights, with and without control of the actual times of flights.

## Slide 6: Method—Data-driven dynamics

## Slide 7: Method—Data-driven dynamics
Three most important assumption to estimate the needed probabilities:
  Each record is a single event and only related to others by connection edges, regardless the time of the delay
  All flights and airlines are assigned to the same time interval between the arrival of the previous flight and the departure of the next flight. After this interval expired all flights depart at the same time.
  The records of flights that have same departure and arrival airport are merged.

## Slide 8: Method—Data-driven dynamics
Create the flight delay network for an airline from FDC dataset, including the associated adjacency matrix of connection edges E
Using the data driven dynamics CARP to simulate all flight in the network and the dynamics of flight delays.
  Randomly assign the delay status of each flight according to its probability estimated, and rest of flights’ status are on time at initial state

## Slide 9: Method—Optimal Control of flight delay network
Find the optimal sequence of input signals , which minimize the function which take involved state and input signals within time steps as parameters.
Three steps:
  Linearization
  Linear quadratic regulator (LQR)
  Total operating cost

## Slide 10: Method—Optimal Control of flight delay network
Linearization:
  Why linearization: nonlinear functions and are hard to solve
  How: linearize those functions at operating point (
  Result: the real-time control strategy.

## Slide 11: Method—Optimal Control of flight delay network
Linear quadratic regulator (LQR)
  Minimize the quadratic function of the state vector and the control input
  The cost at the final time step:
  The stage cost at :

## Slide 12: Method—Optimal Control of flight delay network
Continue the LQR:
  Matrices
  The average delay cost for each flight is per delay hour
  The average delay cost to a passenger , where is average delay time for each flight i.
  The average rent cost of a plane is per hour
  The rental cost of a replacement plane is , where is average flight time of each flight

## Slide 13: Method—Optimal Control of flight delay network
Total operating cost
  Linear function for the total operating cost:
  Two components:
    Expected delay cost and plane renting cost
  Application: quantification of the performance of the optimal control or no control strategies.

## Slide 14: Result—Optimal control for the sample flight delay network
Realistic example of five flights of United Airlines (UA)
Figure 2 A, C are results without control, Figure 2 B, D with control

## Slide 15: Result—Optimal control for the real airline flight delay network
Figure 3 represent the results of all 13 US domestic passenger airlines, with and without control

## Slide 16: Result—Optimal control for the real airline flight delay network
Figure 4 A,C,E represents the reduction of delay costs on all airlines in the United States and departing from LAX and JFK by optimal control.
Fig. 4 BDF shows the relative cost reduction by LQR.

## Slide 17: Discussion
The new framework provide a path that transit a flight delay problem into a standard model of a complex machine. So the problem becomes how to optimal drive the machine.
By applying control theory, the optimal solution is found.
Future works:
  Will address related issues to make the framework more applicable in the future.
  Control of coordinated delays
  Design a direct solver for non-linear dynamics models

## Slide 18: reference
Xiang Niu, Chunheng Jiang, Jianxi Gao, Gyorgy Korniss & Boleslaw K. Szymanski. From data to complex network control of airline flight delays. Nature, 2021. From data to complex network control of airline flight delays | Scientific Reports (nature.com)

## Slide 19: Thank you